Demonstrating Shiva v0.13 Alpha
        By Ryan O’Neill

---
State of the art ELF patching solution
A practical approach to patching native software in Linux
Natural patch development in C code
ELF symbol and relocation driven patching operations
An ELF runtime transformation technology
Loads and links relocatable ELF patches at runtime
Introduces new linking concepts for program transformation

---
Shiva design goals for phase-2
Flexible and modular micropatching system
Specialized ELF interpreter “/lib/shiva”
Program transformation at runtime with relocatable objects and ELF ABI extensions (i.e. transformations, linker chaining, etc.)
Versatile patching capabilities
Relink any part of a programs code or data symbolically
Splice operations: Insert symbolically rich C code anywhere
Transformation operations with C macros
The ability to install many patches successively

---
ELF ABI compatibility
Shiva fits into the ELF ABI toolchain
Compiler: gcc/clang
ELF Linker: “/bin/ld”
ELF Dynamic linker: “/lib64/ld-linux.so”
Shiva (Custom dynamic linker): “/lib/shiva”

---
ELF ABI extensions
Shiva extrapolates on existing ELF ABI
ELF Transforms
Chained dynamic linkers (aka ELF interpreter chaining)
Cross ELF Relocations
Delayed ELF relocations
LDSO ELF meta-data programming
Shiva patch prelinking
Updates dynamic segment with patch-file meta-data
Updates PT_INTERP segment with path to “/lib/shiva”
Adds an extra PT_LOAD segment
Generates control flow and XREF data
Creates custom ELF sections .shiva.xref, .shiva.branch, .shiva.strtab

---
Shiva ELF linking workflow